Fuszenecker Róbert
2011.
Microcontroller programming

---
Embedded systems
An embedded system is a
- computer system
- designed to perform one or few dedicated functions
- often with real-time computing constraints.
Definition: from Wikipedia.

---
Embedded systems
Typical types of embedded systems:
- Industrial computer,
- System on module, computer on module,
- Microcontroller,
- FPGA.

---
Industrial computers

---
System on modules

---
Microcontrollers

---
FPGAs
FPGA: Field Programmable Gate Array

---
Embedded operating systems
- Industrial computers and system-on-modules are based on 32-bit processors (with MMU) and have enough resources to run operating systems, i.e. Linux or Windows CE.
- Microcontrollers sometimes run real-time operating systems: FreeRTOS, QNX Neutrino, etc.
- FPGAs generally don't run anything,
  in certain cases they realize soft microprocessors that may run Linux: MicroBlaze, NIOS 2.

---
ARM cores
ARM Holdings don't produce any silicon chips, they design only the core of the processors.
ARM: Advanced RISC Machine.

---
ARM cores

---
ARM cores
There are 3 kinds of ARM cores:
- Application processors (can run Linux).
  - Cortex-A8 (single core), Cortex-A9 (dual or quad core),
  - Cortex-A15 (quad core, servers),
- Microcontroller cores.
  - Cortex-M3, Cortex-M1 (low power), Cortex-M0 (FPGA),
- Obsolete cores (not recommended for new designs),
  - ARM7, ARM9, ARM11.

---
Processor modes (Cortex-A)
- Abort Mode,
- Fast Interrupt Mode (FIQ),
- Interrupt Request Mode (IRQ),
- Supervisor Mode (kernel),
- System Mode (similar to User Mode),
- Undefined Mode,
- User Mode (user space applications),
- Monitor Mode (debug).

---
Processor modes (Cortex-M)
- Thread mode (to execute application software),
- Handler (interrupt and exception handlers),
- Supervisor mode (after RESET).
Generally, “thread mode” is not used in embedded systems.

---
Register set
ARM processors have 16 × 32 bit registers, many of them has special functions:
- R15: instruction pointer,
- R14: link register,
- R13: stack pointer,
- R11: frame pointer (optional).
The other ones are general purpose registers.

---
Register set (Cortex-A)

---
Register set (Cortex-M)

---
Instruction set
- ARM Cortex-A cores support both ARM (32 bit) and THUMB (16 bit) instructions (as well as many floating point, DSP and SIMD instructions).
- ARM Cortex-M cores support THUMB2 (16 or 32 bit) instructions only.
THUMB2 instructions are the 16 or 32 bit equivalent of the 32-bit ARM instructions. They are used to save memory in resource-critical applications (μC).

---
Instruction set
ARM instruction example (always encoded as a 32-bit word):
e08631a7 add r3, r6, r7, lsr #3
THUMB2 instruction examples (16 or 32 bit, depends on the instruction itself):
        683a ldr r2, [r7, #10]
        fbc3 1204 smlal r1, r2, r3, r4

---
Memory map (Cortex-M)

---
Interrupt vectors (Cortex-A)
Physical Address	Vector name
0x0000'0000	Reset
0x0000'0004	Undefined instruction
0x0000'0008	Software interrupt
0x0000'000C	Prefetch abort
0x0000'0010	Data abort
0x0000'0014	(not used)
0x0000'0018	IRQ
0x0000'001C	FIQ

---
Interrupt vectors (Cortex-M)
Physical Address	Vector name
0x0000'0000	Initial SP
0x0000'0004	Reset Handler
0x0000'0008	NMI Handler
0x0000'000C	Hard Fault Handler
0x0000'0010	Memory Management Handler
0x0000'0014	Bus Fault Handler
0x0000'0018	Usage Fault Handler
...	...
0x0000'0040	Hardware Interrupt 0
0x0000'0044	Hardware Interrupt 1
...	...
0x000'003FC	Hardware Interrupt 243

---
Booting the processor (Cortex-A)
- After the RESET event the Cortex-A* processor starts to execute the instruction that can be found at address 0x0000'0000.
- This is typically an unconditional jump to the ROM code that loads the “real” boot loader.
00000000 ldr pc, [pc, #ROM_CODE]
The boot loader should be able to load and start the Linux kernel or anything else.

---
Booting the processor (Cortex-M)
- The 0th element of the vector table is the initial value of the stack pointer: usually the last addressable cell of the internal RAM.
- The 1st item is the RESET vector, this is an ADDRESS that points to the “main” function.

---
Booting the processor (Cortex-M)
__attribute__ ((section(".interrupt_vector")))
void (*const Vectors[])(void) = {
   (void *)0x20003FFC // The initial stack pointer
   Reset_Handler, // The reset handler
   ...	// Other interrupt handlers
};
extern int main(void);
void Reset_Handler(void) {
   While(1) {
       main();
   }
}

---
The main() function
- Since the stack pointer is set up by the hardware, the processor core is ready to start the “real” task.
- Typically the main() function
  - sets up the hardware peripherals (by using the Firmware library),
  - the interrupt controller,
  - optionally the Memory Protection Unit,
  - and waits for interrupts (low power mode).

---
Memory mapped I/O
- Several “memory cells” are directly connected to hardware peripherals.
- Hardware registers can be accessed by (memory) read and write instructions, similarly to RAM operations.
- Hardware registers can be protected by the Memory Management Unit (permission control) or the Memory Protection Unit (MPU).

---
Accessing HW registers
#define ADC_BASE_ADDRESS 0x4000A000
#define ADC_START_CONVERSION 0x00000004
typedef struct {
    uint32_t adc_status;
    uint32_t adc_value;
    uint32_t adc_error;
} adc_hw_t;
adc_hw_t *adc0 = (adc_hw_t *)ADC_BASE_ADDRESS;
adc0->adc_status |= ADC_START_CONVERSION;
return_value = adc0->adc_value;

---
Firmware library
- The firmware library is provided by the chip manufacturer (hardware-dependent).
- Contains high level interface to hardware registers:
  - Names instead of addresses (#define),
  - Functions to manipulate the HW registers.
- Sometimes a digital signal processing library is included, so that the programmer doesn't need to work with assembly instructions.

---
Firmware library example
int main()
{
    SysCtlPeripheralEnable(SYSCTL_PERIPH_GPIOA);
    GPIOPadConfigSet(GPIO_PORTA_BASE, GPIO_PIN_3,
        GPIO_STRENGTH_8MA, GPIO_PIN_TYPE_OD);
    GPIOPinTypeGPIOOutput(GPIO_PORTA_BASE, GPIO_PIN_3);

---
Firmware library example
    SysTickPeriodSet(SYS_TICK_PERIOD);
    SysTickIntRegister(systick_handler);
    SysTickIntEnable();
    SysTickEnable();
    IntMasterEnable();
    for (c = 0; ; c++) {
        counter += c;
        asm("wfi");
    }
}

---
Firmware library example
volatile unsigned int pin_data = 0;
volatile int counter;
void systick_handler()
{
    pin_data = GPIO_PIN_3 - pin_data;
    GPIOPinWrite(GPIO_PORTA_BASE, GPIO_PIN_3, pin_data);
    counter++;
}

---
With “volatile”
  for (c = 0;; c++) {	R2: counter
    counter += c;	R3: &counter
     104: 681a ldr r2, [r3, #0]	R4: c
     106: 18a2 adds r2, r4, r2
     108: 601a str r2, [r3, #0]
    asm("wfi");
     10a: bf30 wfi
     10c: f104 0401 add.w r4, r4, #1
     110: e7f8 b.n 104 <main+0x64>

---
Without “volatile”
  for (c = 0;; c++) {
    counter += c;
    asm("wfi");
      fc: bf30 wfi
      fe: e7fd b.n fc <main+0x5c>

---
Compiling the sources
- Commercial compilers:
  - ARM RVDS,
  - Keil,
  - CrossWorks,
  - etc.
- Open source compilers:
  - gcc,
  - clang/llvm.

---
Compiling the sources (gcc)
With cross-compiled gcc:
Compiling the source code:
gcc -march=arm -c -o crt.o crt.c
Linking the objects:
ld -T cm3.ld -o fw crt.o \
main.o fwlib.a
Converting to the appropriate format
objcopy -O binary fw fw.bin

---
Compiling the sources (LLVM)
With LLVM (not cross-compiled):
Compiling the C source code:
clang -emit-llvm -c main.c
Translating the LLVM object:
llc -march=thumb -mcpu=cortex-m3 \
-o main.s main.ll
Compiling the assembly source:
as -o main.o main.s

---
Compiling the sources (LLVM)
Linking the object files and the driver library
(the same as the gcc way):
ld -T cm3.ld -o fw crt.o \
main.o fwlib.a
Generating binary output file (FLASH image):
objcopy -O binary fw fw.bin

---
Behind the scenes: linking
- There are sections in the object files, i.e.:
  - Code (.code; the instructions to be run)
  - Data (.data, .bss; global and static local variables)
  - Read-only data (.rodata; const values, initial values of global variables)
  - Debug information (.debug_info, .debug_line, ...)
  - Interrupt vectors section (.interrupt_vector – defined by us:
__attribute__((section(“.interrupt_vector”)))

---
Behind the scenes: linking
- Sections in executable files:
  - Sections of the object files should be merged,
  - Sections should be reordered according to the linker script,
  - Function calls, variable access should be resolved,
- Linker scripts
  - Defines the sections (and their order) of the executable files.

---
Linker scripts
MEMORY
{
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x40000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x10000
}

---
Linker scripts
SECTIONS
{
   .text :
   {
   *(.stack_pointer)
   *(.interrupt_vector)
   _text = .;
   *(.text .text.*)
   *(.rodata .rodata*)
   _etext = .;
   } > FLASH
.bss : AT (_etext)
   {
   _data = .;
   *(.data .data.* .bss .bss.*)
   _edata = . ;
   } > SRAM

---
After linking
cortex-m3: file format elf32-littlearm
Sections:
Idx Name Size VMA LMA File off Algn
  0 .text 00002674 00000000 00000000 00008000 2**2
        CONTENTS, ALLOC, LOAD, READONLY, CODE
  1 vtable 0000011c 20000000 00002674 00010000 2**2
        CONTENTS, ALLOC, LOAD, DATA
  2 .bss 00000008 2000011c 00002790 0001011c 2**2
        ALLOC, LOAD, DATA

---
Debug
- We can use a simulator to debug our code:
  - gdb's built-in simulator (emulates a processor),
  - qemu (emulates a complete device),
- Or we can use the target hardware to debug the firmware; we need
  - a program to download the FLASH content (firmware),
  - a gdb-proxy (which communicates with the hardware),
  - the gdb (GNU's debugger; ARM version),
  - optionally an IDE.

---
Debugger operations
- Step-by-step C/C++ code analysis
- Breakpoints on instructions
- Watchpoints on variables
- Step-by-step assembly code analysis
- Memory and register dump

---
Programming languages
Can we use programming languages other than C?
- Industrial computers and system-on-modules boot Linux or Windows CE, thus the answer is: yes.
- C++(0x) code for microcontrollers is not rare, but C# (.NET micro framework) is not really used.
- If the FPGA realizes a soft processor, any languages can be used.

---
Difficulties with C++
- No memory management
  [operator new() and operator delete() can be implemented],
- Exception handling is problematic,
- Virtual function calls are difficult to implement,
- GNU's libstdc++ is not enough resource-efficient,
  - But we can use CLANG's libstdcxx instead of GNU's libstdc++.

---
Questions?

---
Thank you for your attention!

---
References
- Cortex™-A8 Technical Reference Manual (Revision: r3p2)
- Cortex™-M3 Technical Reference Manual (Revision r2p1)
- ARM Architecture Reference Manual ARMv7-A and ARMv7-R Edition
- ARMv7-M Architecture Reference Manual